SAFE JOB ANALYSIS

Operation of Bruker D8 X-ray diffractometer

Diff 5, room ØU34

| Subtask | What may go wrong | How to prevent consequences of this |
| --- | --- | --- |
| Opening the radiation safety cabinet | X-ray exposure is possible if the safety circuits fail or are deliberately bypassed | Press the “open doors” button to close the shutter before opening the doors Do not attempt to bypass the safety circuits without permission from the radiation safety officer (Anja Olafsen Sjåstad) |
| Changing Samples and other work inside radiation safety cabinet | The robot may cause injury if moving | Check that robotic sample changer is not moving before changing samples, cleaning etc. |

Safe System of Work- changing samples on the D8 XRD instruments

- Only trained users should open the radiation safety cabinets

- Training will be carried out by Per Fostervoll or David Wragg

- Do not attempt to bypass the safety circuits

- Close the shutter with the “open doors” button before opening the doors

- Change the sample (or carry out other work)

- Close the cabinet with care