SAFE JOB ANALYSIS

Operation of Huber G670 X-ray diffractometer

Room ØU34

| Subtask | What may go wrong | How to prevent consequences of this |
| --- | --- | --- |
| Opening the radiation safety cabinet | X-ray exposure is possible if the safety circuits fail or are deliberately bypassed | Close the shutter before opening the doors Do not use the key to bypass the safety circuits without permission from the radiation safety officer (Anja Olafsen Sjåstad) |
| Alignment of X-ray equipment with beam | X-ray exposure | Only to be carried out by X-ray lab staff Always close the radiation cabinet as much as possible when the beam is on Where possible use the instrument mounted fluorescent screens rather than the hand held one |

Safe System of Work- changing samples on the Huber G670 XRD instrument

- Only trained users should open the radiation safety cabinets

- Training will be carried out by Per Fostervoll, Pavel Karen or David Wragg

- Do not attempt to bypass the safety circuits

- Close the shutter using the measurement software or the button on the instrument LCD control panel before opening the doors

- Change the sample (or carry out other work)

- Close the cabinet with care