SAFE JOB ANALYSIS

Operation of Panalytical Empyrean Thin Film Instrument

| Subtask | What may go wrong | How to prevent consequences of this |
| --- | --- | --- |
| Opening the radiation safety cabinet | Not possible to open cabinet while shutter open, the “open doors” button is deactivated while shutter is open | Do not attempt to bypass the safety circuits |

Safe System of Work- changing samples on the Empyrean instrument

- Only trained users should open the radiation safety cabinets

- Training will be carried out by Øystein Slagtern Fjellvåg or David Wragg

- Check that the instrument is not busy or don’t carry out any commands

- If the instrument is busy, wait or stop the measurement

- Press the “open doors”

- Open the doors

- Change the sample or optics (or carry out other work)

- Close the cabinet with care