SAFE JOB ANALYSIS

Operation of Bruker D5000 X-ray diffractometers

Diff 1, 2 and 3, room ØK54

| Subtask | What may go wrong | How to prevent consequences of this |
| --- | --- | --- |
| Opening the radiation safety cabinet | X-ray exposure is possible if the safety circuits fail or are deliberately bypassed | Close the shutter and switch the X-ray generator to standby before opening the doors Do not attempt to bypass the safety circuits without permission from the radiation safety officer (Anja Olafsen Sjåstad) |
| Alignment of X-ray equipment with beam | X-ray exposure | Only to be carried out by X-ray lab staff Always close the radiation cabinet as much as possible when the beam is on Where possible use the instrument mounted fluorescent screens rather than the hand held one |
| Changing samples and other work inside the cabinet | Goniometer motors can be moved when the doors are open- possible risk of injury | Do not open the cabinet when the goniometer arms are moving Do not move the goniometer drives when someone is working in the cabinet |

Safe System of Work- changing samples on the D5000 XRD instruments

- Only trained users should open the radiation safety cabinets

- Training will be carried out by Per Fostervoll or David Wragg

- Do not attempt to bypass the safety circuits

- Close the shutter and switch the X-ray generator to standby before opening the cabinets

- Change the sample (or carry out other work)

- Close the cabinet with care and switch the generator back on before starting measurement

Ancillary Equipment: Heat Gun

| Subtask | What could go Wrong | How to prevent consequences of this |
| --- | --- | --- |
| Running and moving the heater | Burns and overheating | Do not touch the heater barrel when hot Always ensure proper air flow (??? Bar of pressure on regulator) before starting heater. |